## Slide 1: MQTT
IoT protocol
MQTT library is available on NPM
https://www.npmjs.com/package/mqtt
MQTT Broker:
https://www.npmjs.com/package/mosca

## Slide 2: How to setup MQTT Demo 01
https://github.com/usmcs-pdcc/mqtt-demo-01

## Slide 3: MQTT
Design&Implementation: 1
mqtt-sn.js
broker-mongodb.js
mqtt-client.js
PC
Galileo/Edison

## Slide 4: Download and install MongoDB
https://www.mongodb.com/download-center#community

## Slide 5: Create directory: C:\data\db
Open Command prompt: $ mkdir C:\data
$ mkdir C:\data\db

## Slide 6: Run MongoDB (mongod.exe)
$ "C:\Program Files\MongoDB\Server\3.2\bin\mongod.exe" --dbpath "C:\data\db"
MongoDB is successfully running.

## Slide 7: Verify:
MongoDB ready to receive connection. Please note that by default MongoDB runs on port 27017.

## Slide 8: Run broker-mongodb.js

## Slide 9: Set Broker IP Address in broker-mongodb.js
p/s: Make sure to set IP for broker-mongodb.js accordingly to your PC IP (run ipconfig in cmd).

## Slide 10: Resolve dependencies: broker-mongodb.js

## Slide 11: Run broker-mongodb.js
p/s: Windows might asks you (prompt) to allow Firewall access, so kindly allow it. Notice that Broker (broker-mongodb.js) runs on port 1883.

## Slide 12: Verify: broker-mongodb.js
Broker use MongoDB to store the data. ESTABLISHED means broker is hooked up to MongoDB now.
Broker is ready to receive connection from either SN (Sensor Node, mqtt-sn.js) or client (mqtt-client.js)

## Slide 13: Run mqtt-client.js

## Slide 14: Set Broker IP Address in mqtt-client.js
p/s: Make sure to set IP for mqtt-client.js accordingly to your PC IP (run ipconfig in cmd).

## Slide 15: Resolve dependencies: mqtt-client.js

## Slide 16: Run mqtt-client.js
p/s: When you run mqtt-client.js, your broker (broker-mongodb.js) will immediately receives the connection.

## Slide 17: Verify:
Broker received connection from client (mqtt-client.js).
p/s: To make it real, you may setup mqtt-client.js on other PC.

## Slide 18: Run mqtt-sn.js

## Slide 19: Transfer mqtt-sn.js & package.json into Galileo/Edison

## Slide 20: Set Broker IP Address into mqtt-sn.js
p/s: Access terminal of Galileo/Edison (PuTTY or SSH) first. You can use vim to edit mqtt-sn.js.

## Slide 21: Resolve dependencies: mqtt-sn.js

## Slide 22: Run mqtt-sn.js

## Slide 23: Verify:
p/s: You should be able to see your SN(Sensor Node) connected to broker.

## Slide 24
mqtt-sn.js
mqtt-client.js
broker-mongodb.js
Successful deployment